## Slide 1
UNLIMITED SAMPLING
An exploration of the paper “Unlimited Sampling Beyond Modulo” by Azar, Mulleti & Eldar (2025)
DOMINGO, EDWARD JOHN

## Slide 2
The Dynamic Range Problem
Signals have finite energy
Analog-to-Digital Converters (ADCs) have a finite Dynamic Range.
Notes: ADCs turn a continuous signal into discrete samples that a computer can process.
SR: how often it measures the signal. Sample too slowly and you lose detail - the Nyquist rate sets the minimum needed to capture a bandlimited signal faithfully.
DR: the amplitude window the ADC can actually represent, say .
When a signal exceeds that range, a conventional ADC clips it — flattening everything past and permanently losing that information.
The usual fixes all cost something. You can crank up the sampling rate, but that's expensive in power and hardware. So the question is: can we recover the full signal without paying that price?
In this presentation we explore the B²R² algorithm by Azar, Mulleti, and Eldar — an unlimited sampling framework that recovers the signal perfectly while sampling just barely above the Nyquist rate.
Analog-to-digital converters (ADCs) are the bridge between the analog world and the digital one — they turn continuous signals into samples a computer can process.
An ADC has two "knobs." The first is the sampling rate: how often it measures the signal. Sample too slowly and you lose detail — the Nyquist rate sets the minimum needed to capture a bandlimited signal faithfully. The second is the dynamic range: the amplitude window the ADC can actually represent, say [−ⓜ,𝜆𝜆].
When a signal exceeds that range, a conventional ADC clips it — flattening everything past 𝜆and permanently losing that information.
The usual fixes all cost something. You can crank up the sampling rate, but that's expensive in power and hardware. So the question is: can we recover the full signal without paying that price?
In this presentation we explore the B²R² algorithm by Azar, Mulleti, and Eldar — an unlimited sampling framework that recovers the signal perfectly while sampling just barely above the Nyquist rate.

## Slide 3
Operators
Different ways of processing signals
Notes: So how do we deal with a signal that exceeds the dynamic range?
Instead of just clipping it, we apply a nonlinear operator before sampling.
Clipping is the conventional one — anything above gets pinned to , anything below to . Simple, but it throws information away.
**Modulo** is the one we'll focus on. Instead of flattening the signal, it *folds* it back into the range — every time the signal crosses , it wraps around to and keeps going. Notice nothing gets clipped flat; the orange signal still uses the full range. The information isn't destroyed, just disguised — and that's what lets us recover it later.
μ-law modulo adds a companding step after folding, boosting small amplitudes so they sit better above the noise floor. It's a generalization — and that's the key insight of the paper: clipping, modulo, and companding are all special cases of one general operator .
For the rest of this talk, we'll stick with plain modulo.
So how do we deal with a signal that exceeds the dynamic range? Instead of just clipping it, we apply a nonlinear operator before sampling. Here are three.
Clipping is the conventional one — anything above 𝜆gets pinned to 𝜆, anything below −𝜆to −𝜆. Simple, but it throws information away.
**Modulo** is the one we'll focus on. Instead of flattening the signal, it *folds* it back into the range — every time the signal crosses 𝜆, it wraps around to −𝜆and keeps going. Notice nothing gets clipped flat; the orange signal still uses the full range. The information isn't destroyed, just disguised — and that's what lets us recover it later.
μ-law modulo adds a companding step before folding, boosting small amplitudes so they sit better above the noise floor. It's a generalization — and that's the key insight of the paper: clipping, modulo, and companding are all special cases of one general operator 𝒢_𝜆.
For the rest of this talk, we'll stick with plain modulo.

## Slide 4
Solving for z gets you f
Whatever the non-linearity, the unknown is always z
For modulo:
Notes: Here's the central idea.
We fold samples and collect those values
In the case of modulo, it has a structure 2_lambda times an integer
So we don’t have to directly recover the true signal. If getting the residual is easier, then the true signal itself is solved.

## Slide 5
Time-Domain Separation
Bandlimited finite-energy signals decay
There exists an integer such that the samples stay within the bandlimit beyond it.
Beyond it:
The residual is time-limited to the finite index set and at most has non-zero entries.
Notes: So how do we pin down ? It comes from two properties that let us separate it from the true signal — one in time, one in frequency. This is the first
.
A bandlimited, finite-energy signal decays — by the Riemann–Lebesgue lemma, it has to go to zero as you move out in time. So for any threshold , there's some index beyond which the signal never exceeds the dynamic range again.
And if the signal stays inside , there's nothing to fold. So beyond , the folded samples equal the true samples, and the residual is exactly zero — that's the shaded region versus the tails in the plot.
The payoff: isn't some arbitrary infinite sequence. It's time-limited — at most nonzero entries, all bunched in the middle where the signal was large. We've turned an infinite unknown into a finite one.
Next we'll use the frequency domain to actually solve for those entries.
So how do we pin down 𝑧? It comes from two properties that let us separate it from the true signal — one in time, one in frequency. This is the first
.
A bandlimited, finite-energy signal decays — by the Riemann–Lebesgue lemma, it has to go to zero as you move out in time. So for any threshold 𝜆, there's some index 𝑁_𝜆beyond which the signal never exceeds the dynamic range again.
And if the signal stays inside ±𝜆, there's nothing to fold. So beyond 𝑁_𝜆, the folded samples equal the true samples, and the residual is exactly zero — that's the shaded region versus the tails in the plot.
The payoff: 𝑧isn't some arbitrary infinite sequence. It's time-limited — at most 2𝑁_𝜆+1nonzero entries, all bunched in the middle where the signal was large. We've turned an infinite unknown into a finite one.
Next we'll use the frequency domain to actually solve for those entries.

## Slide 6
Fourier-Domain Separation
The spectral energy in the band-gap region is “purely” the residual
Sampling above the Nyquist rate leaves a band-gap region .
Taking the DTFT and using linearity, only the residual survives within the vacant band.
Notes: Fourier-Domain Separation
Next property → Fourier domain
DTFT of original (top): energy within omega_m band, bandlimited, zero above omega_m
Sampling above Nyquist → band-gap region rho (between omega_m and omega_s/2), spectrum empty
Folding = nonlinearity → generates new spectral content
DTFT of folded (bottom): no longer bandlimited → energy spills into band-gap
Key: original contributes nothing in band-gap → energy there is purely residual (folded minus original)
Linearity → folded spectrum equals residual spectrum in the vacant band
Band-gap = clean window onto residual → reconstruction exploits this
That's the second piece, and it's where "beyond bandwidth" earns its name.
When we sample above the Nyquist rate, the true signal only occupies the band up to 𝜔_𝑚— it's zero in the gap between 𝜔_𝑚and half the sampling rate. You can see it in the top plot: the original signal's spectrum sits entirely inside ±𝜔_𝑚, and the shaded band-gap region is empty.
But the residual 𝑧is **not** bandlimited — folding adds sharp jumps, which spill energy across all frequencies. So look at the bottom plot: once we fold, that vacant band fills up. And by linearity, whatever spectral energy lives in the gap can *only* have come from the residual — the true signal contributes nothing there.
That gives us a clean equation: in the band-gap, the folded spectrum equals the residual's spectrum, 𝐹_𝜆=𝑍.
Now put the two properties together. In time, 𝑧has only 2𝑁_𝜆+1unknowns. In frequency, we have clean measurements of 𝑧in the gap. Finitely many unknowns, plenty of equations — so we can solve for 𝑧.

## Slide 7
Combining the Two
Can we solve for z via matrix inversion?
Sampling frequencies in the bandgap gives the linear system:
Solving for the residuals is a matter of inverting :
Notes: On the band-gap, the folded spectrum is just the DTFT of the residual z (finite sum over the residual samples)
Sample M frequencies in the band-gap (M = 2 N_lambda + 1) → gives a linear system
The system: V z = b
  V = matrix of complex exponentials (the sampled frequencies)
- z = residual samples we want to recover
b = folded spectrum values measured in the band-gap
Solving for the residuals = inverting V → z equals V-inverse times b So in principle, recovering the residual is a direct matrix inversion
So we have finitely many unknowns and clean measurements in the gap. The most direct way to solve is just linear algebra.
In the band-gap, the folded spectrum is a finite sum over the 2𝑁_𝜆+1residual samples — each weighted by a complex exponential. That's a system of linear equations.
Pick 𝑀=2𝑁_𝜆+1frequencies in the gap — exactly as many equations as unknowns. Stack them up and you get 𝑉𝐳=𝐛: the matrix 𝑉holds the exponentials, 𝐳is the residual we want, and 𝐛is the folded spectrum we measured.
𝑉is a Vandermonde matrix — and as long as the frequencies are distinct, it's invertible. So in principle, recovery is just 𝐳=𝑉^(−1) 𝐛.
Clean, but there's a catch — and it's why this isn't the algorithm we actually use.

## Slide 8
Matrix Inversion
Unstable for high
As grows, becomes ill-conditioned
Notes: Here's the catch. "Invertible in principle" and "stable in practice" are not the same thing.
As N_
Here's the catch. "Invertible in principle" and "stable in practice" are not the same thing.
Watch what happens as we shrink 𝜆. A smaller dynamic range means more folds, which means a larger 𝑁_𝜆— and a bigger Vandermonde matrix. On the left, 𝜆=0.25, 𝑁_𝜆=4: recovery is perfect, error is essentially machine precision.
But look at the condition number 𝜅across the panels — it explodes. Eleven, then seventeen hundred, then three hundred *thousand*. By the right-hand panel the inversion has completely diverged — the recovery shoots off the chart while the true signal sits quietly in the middle.
That's the signature of an ill-conditioned matrix: tiny numerical errors get amplified enormously, and in any real setting with noise, it's hopeless.
So Vandermonde inversion is fine as a proof of concept, but it doesn't scale. We need a solver that finds the same residual 𝑧without ever forming or inverting 𝑉— and that's B²R².

## Slide 9
B2R2 Algorithm – Inner Loop
Beyond Bandwidth Residual Reconstruction
Over the band-gap:
Objective:
Gradient:
PGD Inner Loop – repeat to convergence:
Gradient-step:
Project to support:
THE HIGHPASS FILTER
keeps only frequencies in
Notes: - Frame it as an optimization problem.
- folded spectrum = residual spectrum
- That means, instead of perfectly looking for the equality, we would want to minimize the difference of the DTFT of the two within rho.
- The gradient is then the highpass filter between these two.
- The highpass filter operator takes the DTFT of the difference, keeps only the frequencies in rho, then inverses that back to the time domain sample values.
- We can then use this gradient in an iterative way.
So how do we find the same 𝑧without ever touching 𝑉? We recast it as an optimization problem.
We still use the same fact — in the band-gap, the folded spectrum equals the residual's spectrum. But instead of demanding exact equality at a few points, we ask: which 𝑧makes the folded and residual spectra agree as closely as possible **across the whole gap**? That's the objective — minimize the squared mismatch ∥ℱ_𝜌 𝐟_𝜆−ℱ_𝜌 𝐳∥^2, subject to 𝑧living on its known finite support.
We solve it with projected gradient descent — two steps, repeated. Take a gradient step downhill, then project back onto the support: zero out everything outside the 2𝑁_𝜆+1window where we know 𝑧has to live.
And here's the elegant part. The gradient operator ℱ_𝜌^∗ ℱ_𝜌is just a **highpass filter** — it keeps only the band-gap frequencies. So every iteration is a filter plus a masking step. No matrix to build, no matrix to invert, nothing to blow up. The whole thing is convolutions — stable, cheap, and it scales to large 𝑁_𝜆where Vandermonde fell apart.

## Slide 10
Inner PGD Loop
Set-up

## Slide 11
Inner PGD Loop
Set-up

## Slide 12
Inner PGD Loop
Set-up

## Slide 13
Inner PGD Loop
Set-up

## Slide 14
Inner PGD Loop
Set-up

## Slide 15
Inner PGD Loop
Set-up

## Slide 16
Inner PGD Loop
Set-up
Trust only the edges of the supports
Notes: So we run the inner loop — a thousand iterations of filter-and-project. And here's what comes out.
Look closely. At the edges of the support, around , the recovery tracks the true signal beautifully. But toward the middle, where the signal swings hardest and the folds pile up, it falls short — the orange curve flattens out and never reaches those big peaks.
This is the catch with the inner loop on its own: it's accurate at the edges but unreliable in the interior. That's not a bug — it's actually a clue. The residual is easiest to nail down exactly where the signal is just barely crossing , which is at the edges of the active region.
So the strategy — "trust only the edges" — is exactly what the full algorithm exploits. Lock in the residual at the two outermost samples where we know it's right, peel them off, and shrink the problem. Then repeat on a smaller window.
So we run the inner loop — a thousand iterations of filter-and-project. And here's what comes out.
Look closely. At the edges of the support, around ±40, the recovery tracks the true signal beautifully. But toward the middle, where the signal swings hardest and the folds pile up, it falls short — the orange curve flattens out and never reaches those big peaks.
This is the catch with the inner loop on its own: it's accurate at the edges but unreliable in the interior. That's not a bug — it's actually a clue. The residual is easiest to nail down exactly where the signal is just barely crossing 𝜆, which is at the edges of the active region.
So the strategy — "trust only the edges" — is exactly what the full algorithm exploits. Lock in the residual at the two outermost samples where we know it's right, peel them off, and shrink the problem. Then repeat on a smaller window.

## Slide 17
B2R2 Algorithm – Full Loop
Beyond Bandwidth Residual Reconstruction
Initialize:
While
run PGD inner loop
round:
update:
shrink:
Output:
Notes: The full loop
Exploit:
  1. That the residual is structured (at least for the modulo case)
  2. The inner PGD loop solves for the edges first
The
Here's the full algorithm — the inner loop wrapped in an outer one that does exactly that: lock the edges, shrink, repeat.
We start with the folded samples as our first guess and run the PGD inner loop. That gives us a residual estimate that — as we saw — we only trust at the two outermost samples.
Then three quick moves. Round: for modulo, 𝑧has to be an integer multiple of 2𝜆, so we snap the estimate to the nearest valid level — this cleans up small errors completely. Update: subtract the now-known edge residuals off our running estimate. Shrink: those edges are solved, so we narrow the support by one on each side and decrement 𝑁_𝜆.
Look at the diagram — the support sweeps inward, one notch each pass. Solve the edges, peel them off, narrow the window, solve the new edges. We keep going until 𝑁_𝜆hits zero and there's nothing left to unfold.
What's left is 𝐟 ̂— the fully recovered true signal. And because we never built a matrix, the whole thing stays stable no matter how large 𝑁_𝜆started.

## Slide 18
Full B2R2 Implementation
Set-up

## Slide 19
Full B2R2 Implementation
Set-up

## Slide 20
Full B2R2 Implementation
Set-up

## Slide 21
Full B2R2 Implementation
Set-up

## Slide 22
Full B2R2 Implementation
Set-up

## Slide 23
Full B2R2 Implementation
Set-up

## Slide 24
Full B2R2 Implementation
Set-up

## Slide 25
B2R2 vs Matrix Inversion

## Slide 26
Comparison between Operators

## Slide 27
Comparison between Operators

## Slide 28
Conclusion and Next Steps
The B2R2 algorithm can reconstruct a signal to machine precision at just an OF = 2 (for modulo and mu-law modulo)
Test for robustness against noise
Estimate
Notes: The full loop
Exploit:
  1. That the residual is structured (at least for the modulo case)
  2. The inner PGD loop solves for the edges first
The

## Slide 29
Thank you

## Slide 30
#0D1B2A
#1B2A3B
#E8DCC8
#D4621A
#C49A45
Deep Navy
Background
Dark Slate
Surface/card
Warm Sand
Light text
Burnt Orange
Highlight
Muted Gold
Subtle accent
Off-White
Body text
#F2EDE4
Deep Navy
Background
Dark Slate
Surface/card
Warm Sand
Light text
Burnt Orange
Highlight
Muted Gold
Subtle accent
Off-White
Body text